## Slide 1
IoT + WEB APPLICATION + SMART PARKING
Park Ease
Smart Parking Management and Reservation System
First Project Review • MCA 3rd Semester
Project Team: Mithulesh N [25mx328] & Dinesh Kumar S [25mx312]
Project Guide: Dr. A. Sankar
Academic Year: [2025 - 2027]
Live Slots
IoT Sensing
QR Pass
Smart Fare
Notes: Good [morning/afternoon]. I am presenting Park Ease, a Smart Parking Management and Intelligent Reservation System, developed as our MCA 3rd Semester project by myself, Mithulesh N, and my teammate Dineshkumar. This is our first project review, so today I will walk through the problem we identified, our proposed solution, the work completed so far, and a clear roadmap for what remains. Our guide is [Guide Name] from the [Department/College] department.

## Slide 2
THE PROBLEM
Why Conventional Parking Falls Short
No Real-Time Visibility
Drivers waste time searching for a vacant slot with no live availability data.
Manual, Error-Prone Management
Manual tracking of slots and vehicles is slow and inconsistent.
Demand Varies All Day
Parking demand changes hour to hour, so an always-reserved model is impractical.
Revenue Loss from Idle Reservations
Slots held by reservation but left unused reduce operator revenue.
No Overstay / Penalty Tracking
There is no mechanism to monitor overstay or apply violation charges.
Poor User Experience
No simple, unified interface for finding, booking and paying for parking.
Motivation: Park Ease combines peak-hour reservation with off-peak walk-in parking, backed by IoT-based real-time slot monitoring — a practical, hybrid model rather than a rigid, always-reserved system.
2 / 8
Notes: Conventional parking systems suffer from several problems: drivers cannot see live slot availability, manual management is error-prone, and demand for parking is not constant through the day, so keeping every slot reservation-only is impractical and can even cause revenue loss from slots that stay reserved but empty. There is also no built-in way to track how long a vehicle has parked or to apply penalties for overstay. This motivated us to design Park Ease as a hybrid system: reservations during peak hours, and free walk-in access during off-peak hours, all monitored in real time using IoT sensors.

## Slide 3
OUR APPROACH
Objectives & Proposed Solution
OBJECTIVES
Real-time parking slot availability
Reduce time spent searching for parking
Peak-hour reservation, off-peak walk-in
IoT-based vehicle presence detection
QR-based parking acknowledgement
Automatic duration & fare calculation
Penalty handling for overstay/violation
Centralized admin monitoring
PROPOSED SOLUTION — HYBRID MODEL
PEAK
HOURS
1
Select slot & enter vehicle details
2
Pay ₹50 reservation deposit
3
Receive QR parking pass
4
Entry validation → park → exit fare
OFF-PEAK
HOURS
1
Arrive & view available slots
2
Use an available slot directly
3
No advance reservation needed
4
Park → exit → fare calculated
Peak-hour timings and tariff rules are configurable by the administrator.
3 / 8
Notes: Our objectives focus on giving users real-time visibility into parking availability, reducing search time, and automating duration and fare calculation. The core of our proposed solution is a hybrid model. During peak hours, a user reserves a slot in advance by paying a small refundable deposit of 50 rupees and receives a QR parking pass. During off-peak hours, the same user can simply walk in and use any available slot without booking in advance. Both paths converge into the same parking, exit and fare-calculation process, and peak-hour timing and tariffs will be configurable by the administrator.

## Slide 4
END-TO-END FLOW
Complete System Workflow
User opens Park Ease web app
Select parking area → date & time
System checks slot status & shows layout
Within peak hours?
YES
NO
RESERVATION PROCESS
Select available slot
Enter vehicle & contact details
Pay ₹50 reservation deposit
Generate QR parking pass
Entry QR validation
OFF-PEAK PROCESS
Use available slot directly
No advance booking required
Sensor detects vehicle
Slot marked OCCUPIED
Duration tracked → exit → fare + penalty (if any) − deposit adjustment → receipt → slot AVAILABLE
4 / 8
Notes: This diagram shows the complete lifecycle. The user opens the web app, selects a parking area and time, and the system checks whether that slot falls in a peak or off-peak window. If it is peak hours, the reservation path is triggered: slot selection, vehicle details, the 50-rupee deposit, and a QR pass that is validated at entry. If it is off-peak, the user simply walks in and uses an available slot, which the sensor detects directly. Both paths converge at the same point: parking duration is tracked, and at exit the system calculates the normal fare, adds any penalty for overstay, adjusts the deposit if one was paid, generates a receipt, and finally frees the slot.

## Slide 5
PROGRESS REPORT
Work Completed So Far
COMPLETED
Project Planning
Idea finalized: hybrid peak/off-peak model
Complete parking lifecycle designed conceptually
Requirement Analysis
User, availability & reservation requirements defined
Deposit, QR pass, fare & penalty concepts defined
Front-End Development
Initial single-page web app built
Slot availability & selection UI designed
No mandatory login — simple user flow
Hardware Preparation
ESP32, HC-SR04 sensor, breadboard, USB cable collected
Hardware Study
ESP32 GPIO pins & HC-SR04 pins studied
Voltage-divider requirement for ECHO pin identified
Note: IoT sensor data is not yet integrated with the website — this is planned for upcoming phases (see next slides).
5 / 8
Notes: So far, we have finalized the project idea and conceptually designed the complete parking lifecycle. We have completed requirement analysis covering availability, reservation, deposit, QR pass, and fare/penalty concepts. On the front-end, we have built an initial single-page web application with a slot availability and selection interface that does not require mandatory login. On the hardware side, we have collected the ESP32 board, HC-SR04 ultrasonic sensor, breadboard and USB cable, and studied their pin configuration — including identifying that we will need a voltage divider to safely connect the sensor echo pin to the ESP32. I want to be clear that the IoT sensor is not yet integrated with the website — that integration is planned work, which I will cover next.

## Slide 6
ARCHITECTURE
System Architecture & Technologies
HC-SR04 Ultrasonic Sensors
Detect slot occupancy
ESP32 (Wi-Fi)
Reads sensor, sends data
Backend / REST API (Flask)
Business logic & endpoints
MySQL Database
Slots, bookings, payments
Park Ease Web Application
User-facing interface
TECHNOLOGY STACK
Frontend | HTML, CSS, JavaScript (SPA)
Backend | Python Flask, REST APIs
Database | MySQL
IoT | ESP32, HC-SR04, Wi-Fi
Other | QR generation, payment API (planned), parking map UI
HARDWARE STATUS
Components purchased / collected
COMPLETED
Initial circuit design prepared
COMPLETED
Single-sensor prototype testing
IN PROGRESS
6 / 8
Notes: Our architecture has five layers. HC-SR04 ultrasonic sensors detect whether a slot is occupied; this data is read by an ESP32 microcontroller and sent over Wi-Fi to a Flask-based REST API backend, which stores and manages data in a MySQL database, and finally reflects the live status on the Park Ease web application. An admin dashboard sits alongside the backend for monitoring reservations, payments and reports. For technology, our frontend is a single-page HTML/CSS/JavaScript application, the backend is Python Flask, and the database is MySQL. On hardware, we have purchased all components and prepared an initial circuit design; single-sensor prototype testing is our immediate next milestone.

## Slide 7
Project Implementation Timeline
Park Ease – Smart Parking Management and Intelligent Reservation System
ZEROTH REVIEW — PLANNED
FIRST REVIEW — CURRENT STATUS
Requirement Analysis & System Architecture
Planned: 25 JUL 2026
✓
COMPLETED
Completed 25 JUL 2026
Database & Backend Development
Planned: 01 AUG 2026
✓
COMPLETED
Completed 01 AUG 2026
Frontend & UI Development
Planned: 13 AUG 2026
✓
COMPLETED
Completed 13 AUG 2026
IoT Hardware Setup & Sensor Calibration
Planned: 22 AUG 2026
◐
IN PROGRESS
Since 22 AUG 2026
IoT–Backend, QR & Payment Integration
Planned: 05 SEP 2026
○
PENDING
Target 05 SEP 2026
Testing & Deployment
Planned: 12 SEP 2026
○
PENDING
Target 12 SEP 2026
FIRST REVIEW PROGRESS
Park Ease – Smart Parking Management and Intelligent Reservation System
ZEROTH REVIEW — PLANNED
FIRST REVIEW — CURRENT STATUS
Requirement Analysis & System Architecture
Planned: 25 JUL 2026
✓
COMPLETED
Completed 25 JUL 2026
Database & Backend Development
Planned: 01 AUG 2026
✓
COMPLETED
Completed 01 AUG 2026
Frontend & UI Development
Planned: 13 AUG 2026
✓
COMPLETED
Completed 13 AUG 2026
IoT Hardware Setup & Sensor Calibration
Planned: 22 AUG 2026
◐
IN PROGRESS
Since 22 AUG 2026
IoT–Backend, QR & Payment Integration
Planned: 05 SEP 2026
○
PENDING
Target 01 SEP 2026
Testing & Deployment
Planned: 12 SEP 2026
○
PENDING
Target 12 SEP 2026
FIRST REVIEW PROGRESS
3
Completed
1
In Progress
2
Pending

## Slide 8
WRAPPING UP
Expected Outcome & Conclusion
EXPECTED OUTCOME
Real-time availability
Reduced search time
QR-verified entry
Automated fare & penalty
Better operator monitoring
Less manual intervention
CONCLUSION
Park Ease proposes a practical smart parking solution that combines IoT-based real-time occupancy detection with a web-based management system.
The hybrid reservation model avoids keeping slots unnecessarily reserved throughout the day while still offering convenience during peak hours.
Remaining work will focus on hardware integration, backend APIs, database implementation, payment, QR validation, exit fare calculation, penalty handling, and full system testing.
8 / 8
Open Website...
Notes: To summarize, Park Ease is expected to deliver real-time parking availability, reduced search time, QR-verified entry, and automated fare and penalty calculation, giving operators better monitoring with less manual effort. Looking further ahead, we plan enhancements such as a mobile app, automatic number plate recognition, navigation to the parking area, EV charging slot management, predictive availability, and cloud deployment. In conclusion, Park Ease is a practical hybrid smart-parking solution, and our remaining work is clearly scoped across hardware, backend, database, payments and testing. Thank you.